## Slide 1
PROCESS MONITORING & CONTROL

## Slide 2: Planning for a New Tomorrow
Joshua Mellen
Product Manager
Dominion Energy
Bhawuk Luthra
Engineering Consultant

## Slide 3
Bhawuk Luthra, Engineering Consultant Josh Mellen, Product Manager |  |  |  |  |  | 
Planning for a New Tomorrow
― Forecast-Driven Outage Planning for System Operations Center ―
Notes: Title: Planning for a New Tomorrow – Forecast-Driven Outage Planning for System Operations Center
Abstract: Dominion Energy is facing considerable growth across its operating territory – much of it stemming from non-conforming load produced by technology and the EV sector. The need for improved forecasting is becoming a mandatory part of our operations and company decision making in outage planning. In this session, we will discuss strategies and tactics around long-term load forecasts (LTLF) for area, substation and transformer-level forecasting, including the development of an operating framework utilizing Seeq. We will also explore real world case studies on managing and reprioritizing outages, thus enhancing system reliability and operational efficiency.

## Slide 4: Dominion Energy at a Glance
Who we are. Where we reside. What we do.
We are a leading energy company providing clean, safe, and reliable energy to >3.5M customers across the US
Our team is within the Transmission part of the organization, where we own and support applications such as PI, Seeq, Predictive Grid.
We added Seeq to our tech stack in 2023 to help empower our users with low code, no code option for data analytics
DRIVEN BY OUR RELIABILITY OBJECTIVES
Generation
Transmission
Distribution
Customer
Chart: Generation Capacity
| Natural Gas | Nuclear | Solar/Wind | Hydro | Coal
Generation | 0.45 | 0.14 | 0.18 | 0.13 | 0.1

## Slide 5: An Evolving and Present Challenge
Transmission operators across the country are facing the impact of a power-hungry commercial sector.
From the demand side, streaming, artificial intelligence, and commercial EVs are creating influxes of power usage.
Unprecedented growth means unprecedented demand on infrastructure development. Keeping up with demand will require an overhaul of supply chain manufacturing to project deployment all while keeping our rate bases in check.
CHALLENGES DOMINION ENERGY IS FACING
And it’s Newsworthy

## Slide 6: The Importance of Transmission Forecasting
Not All Forecasts are Built the Same. Nor Should They.
Time horizons, service areas, and business objectives can vary.
Transmission can no longer rely on an overengineered grid.
Our Focus for Transmission Today
We’re hyper-focused on our SOC objectives.
We forecast three areas. Over 100 substations. Over 300 transformers.
We’re capturing data from nearly a dozen sources – a complex business challenge in a conventionally siloed organization.
An emphasis on transparency & explainability (non-blackbox).
Integration with our modeling systems including EMS & ANODE
ENTER FORECASTING
Outage Planning
Sales and Revenue
Capital Investment Planning
RTO Projections
“long term”
“short term”
Area Forecast
Constrained Zone
Bus-level
Business Intelligence
15 Year IRP
1 Year

## Slide 7: This is Our Transmission Forecast Story
From Framework to Business Impact
OUR FOUR PART STORY
Our Business Objectives
Building a Sustainable Framework
Enabling Dominion: Applied Forecast Case Studies
Visualization: The Importance of Data Storytelling
Our Business Objectives

## Slide 8
Data Collection
and
Processing
Exploratory
Data Analysis:
Identify Patterns
and
Data Cleansing
Feature
Engineering:
Regressor
and
Scenario
Evaluation
Model Selection:
Explore and
Train Models,
Test Forecast,
Tune Model
Develop
and
Reconcile
Forecast
Feedback:
Deliver Results,
Gather Feedback,
Iterate
Continuous Improvement/Continuous Deployment
FORECASTING FRAMEWORK

## Slide 9: Data Collection & Processing
Challenges & Solutions of Building an Evolving Hierarchy
FRAMEWORK
Challenge: No listing of substations / transformers / delivery points.
Solution: Collaborated w/ other transmission teams (SOC & Planning) to develop a comprehensive list of assets in constrained area and build hierarchy in SeeQ.
Challenge: Limited historical data for delivery points and substations.
Solution: Built automated calculations in SeeQ to estimate missing data for delivery points, transformers, substations, and area-level load.
Data Collection and Processing
Notes: One of the challenges we faced was different definition for operation, agreed upon definition of constrained zone.
The increase in the trend is growth but in reality, it could be missing data.

## Slide 10: Enhancing Data Quality
Aiming to avoid garbage in, garbage out
Visual Inspection
Data Imputation Techniques
Clean Data
FRAMEWORK
Exploratory Data Analysis
Data Ready for Forecasting
Missing Data

## Slide 11: Filtering Techniques for Outlier Detection
Identifying Best Techniques to Clean the data
Filtering Techniques:
Low pass Filter: Captures more Variance in the data
Moving Average: Smoothing the signal
Identify Outliers
FRAMEWORK
Exploratory Data Analysis

## Slide 12: Pattern Recognition to Build Load Profiles
Weekly Seasonality
Daily Seasonality
FRAMEWORK
Feature Engineering
Residential Loads
Variable
Data Center Loads
Consistent
Data Center Load Residential Load
Conforming vs Non-Conforming

## Slide 13: Enabling Dominion
Applied Forecast Case Studies

## Slide 14: Scheduling Outages Intelligently with our RTO
Supporting SOC and PJM in planning and prioritizing outages
Challenges:
Unable to schedule outages as limited data was available to make decision.
CASE STUDY 1
Model Selection
Solution:
Integrated Load Ramp Rate
Analyze System to identify contingencies like thermal and voltage violations with bulk Load.
Studying the impact of solar and scheduling outages to meet the demand.
Results:
Developed Load Forecast.
RTO approved planned outages after rescheduling it during summer months
Plan to add cap bank to support the load
Load Ramp
Raw Data
Data for forecasting
SARIMA Forecast
LINEAR Forecast

## Slide 15: How our Forecast Enabled an SOC Decision
Building Forecast for System Maintenance
CASE STUDY 2
Results:
Line Forecast: Aggressive and Conservative Forecast
Reprioritized Outages
Potential Load Shed
Aggressive
Conservative
Develop Forecast
Challenge:
Identify unprecedented growth.
Solution:

## Slide 16: Visualization
The Importance of Data Storytelling

## Slide 17: Making Forecasts Accessible
We’re serving our data in Power BI displays with intuitive navigation to drive thoughtful analysis
USING VISUALIZATION TO DRIVE DISCUSSION
SUBSTATION 1
TRANSFORMER-1
TRANSFORMER-2
SUBSTATION 2
TRANSFORMER-1
TRANSFORMER-2
TRANSFORMER-3
TRANSFORMER-4
TRANSFORMER-5
SUBSTATION 3
SUBSTATION 4
SUBSTATION 5
SUBSTATION 6
SUBSTATION 7
SUBSTATION 8
SUBSTATION 9
SUBSTATION 10
SUBSTATION 11
SUBSTATION 12
SUBSTATION 13
SUBSTATION 14
SUBSTATION 15
SUBSTATION 16
SUBSTATION 17
AREA 1
AREA 3
AREA 2
It was critical that our data product and data stories be accessible through enterprise tooling to reaching a broader audience that may benefit from the forecasts we produce quarterly.
Feedback
Notes: Framing a story about Forecasting. Multiple Groups are doing forecasting and new tools are coming like Load Seer, different approaches
Which is good as It encourages open discussion about these different narratives.
10% increase in load in next 5 years
Stimulate discussion , steps towards decision working

## Slide 18: Visualizing Growth vs. Forecast
Showing decision-makers and engineers an evolving story of system growth
TRENDS FOR PAST AND FUTURE
New Bulk Load
Actual
Forecast
Actual vs Forecast
Feedback

## Slide 19: Thank You
Questions? Get in touch!
bhawuk.luthra@dominionenergy.com
Josh Mellen
joshua.m.mellen@dominionenergy.com
Bhawuk Luthra